## Slide 1
ParkGrid
Smart Parking Allocation System
IoT / IoE project | QR gate access | ML peak alerts
Team
Reg No - Name
Reg No - Name
Reg No - Name
Reg No - Name
A1
A2
A3
A4
A5
B1
B2
B3
B4
B5
C1
C2
C3
C4
C5
D1
D2
D3
D4
D5
Live slot map: free / booked / occupied
Notes: Title slide. Fill in the four Reg No - Name entries before presenting.

## Slide 2
Problem and goal
2
ParkGrid
The problem
Drivers circle the lot hunting for a free spot
Attendants check tickets and lift barriers
No warning before the lot fills up
Our goal
Book a specific slot in advance
Contactless QR entry and exit, no attendant
Live occupancy plus ML peak alerts
Notes: Frame the problem in one sentence, then the goal. Keep it short.

## Slide 3
What ParkGrid does
Four capabilities, two dashboards
3
ParkGrid
Pre-book a slot
Pick a slot and time; get a signed QR code
Walk-in booking
Guest kiosk, no account, nearest free slot
QR gate access
Scan to enter and exit; gate opens by itself
ML peak alerts
Forecast when the lot will cross 85%
User dashboard
book, QR, history
Monitor
3D lot + live activity log
Admin
free slots for demo resets
Notes: Two dashboards: one for users, one (Monitor) that shows how the system works. Admin is an operator tool.

## Slide 4
System architecture
Hardware is simulated; everything downstream is real
4
ParkGrid
EDGE (simulated)
Sensor simulator
ESP32 + HC-SR04 x20
Gate simulator
servo boom gate
MQTT
broker
(Mosquitto)
BACKEND (FastAPI)
MQTT worker
REST API + JWT
WebSocket hub
ML predictor
PostgreSQL
FRONTEND (React)
User dashboard
Monitor (3D + logs)
Admin
Guest kiosk / Gate
Key idea
The backend only sees MQTT messages, so real ESP32 devices can replace the simulators with no backend change.
Notes: Walk left to right. The MQTT broker is what decouples hardware from software.

## Slide 5
How the IoT layer is simulated
Two Python programs publish real MQTT messages
5
ParkGrid
Sensor simulator
ESP32 + HC-SR04 for each of 20 slots
Simulated clock at 60x speed
Day curve: about 3% at night up to 92% at noon
Raw distance + 30 cm occupied threshold
Gate simulator
Servo boom sweep 0 to 90 degrees and back
Receives open command, sends acknowledgement
Local event log, like device serial output
MQTT topics
Topic | Direction | Carries
parking/sensor/{n}/status | device to backend | distance_cm, occupied
parking/gate/command | backend to gate | open, entry or exit
parking/gate/ack | gate to backend | cycle completed
Design choice
Gate-controlled slots are held occupied so the random simulation never overwrites a real gate scan.
Notes: Emphasise: no real hardware, but the messages are real MQTT, so the backend cannot tell the difference.

## Slide 6
IoT components for a real deployment
Hardware that would replace the simulators (12 components)
6
ParkGrid
ESP32 DevKit
Wi-Fi MCU, one per 4 slots
Arduino Uno / Nano
Simple sensor-node option
Raspberry Pi 4
Gate gateway, camera, broker
HC-SR04 ultrasonic
Slot occupancy, x20
IR obstacle sensor
Vehicle at gate lane, x2
RGB / R-G-Y LEDs
Per-slot status, x20
SG90 / MG996R servo
Boom barrier motor
Pi Camera / webcam
Reads the QR at the gate
OLED / 16x2 LCD
Gate message display
Active buzzer
Accept / reject tone
5 V relay module
Switches barrier power
PSU + buck converter
5 V / 12 V power rails
Also: 220 ohm resistors, logic-level shifter (5 V echo to 3.3 V), Wi-Fi router, enclosures and cabling
Notes: Full table with quantities and wiring notes is in the documentation, section 4.3.

## Slide 7
From sensor to LED
How one slot's state is decided
7
ParkGrid
1
HC-SR04
measures distance to the car
2
ESP32
distance < 30 cm means occupied
3
MQTT
JSON status message, QoS 1
4
Backend
applies state rules, saves to DB
5
LED + UI
slot colour updates live
LED colours
Free
green LED
Booked
red + green mix
Occupied
red LED
Notes: A booked-but-empty slot is expected to look empty to the sensor, so the backend keeps it BOOKED until the car arrives.

## Slide 8
Working: booking to exit
The same QR code opens the gate twice
8
ParkGrid
Book
Pre-book or guest kiosk
Get QR
Signed token on phone
Scan
Gate camera reads QR
Validate
Signature + booking state
Gate opens
Slot turns red, event logged
Slot state machine
FREE
booking created
BOOKED
scan: entry
OCCUPIED
scan again: exit
FREE
Admin can free any slot; unused bookings expire when their window ends.
Notes: Entry and exit use the same QR. The first scan is entry, the next scan is exit.

## Slide 9
QR code and gate validation
Signed tokens, checked on the server
9
ParkGrid
Token anatomy
payload
booking_id, slot_id
+
HMAC signature
(secret key)
eyJib29raW5nX2lkIjoxNH0.zK3...
Why it is safe
Guessing a booking id fails: signature mismatch
Token must equal the one stored for the booking
Validity comes from booking status and time window
Checks at POST /gate/scan
Signature valid?
else 400
Booking found, token matches?
else 404
Not completed, cancelled, expired?
else 409
Pending: entry. Active: exit.
gate command sent
Camera re-reads are ignored for 12 s so one QR is not scanned twice by accident.
Notes: The QR is signed, not encrypted. The scanner ignores the same code for 12 seconds so a lingering QR does not toggle entry into exit.

## Slide 10
Machine learning: data and target
UCI Parking Birmingham dataset (id 482)
10
ParkGrid
35,717
readings
30
car parks
11
weeks, Oct-Dec 2016
30 min
sampling interval
What it predicts
Regression
Occupancy percentage of the lot (0-100%) at a given hour
Classification
Will the next reading reach 85% or more? Drives the peak alert banner
Notes: The dataset has capacity, occupancy and timestamp per car park. We derive percentage occupancy and a next-reading threshold flag.

## Slide 11
ML training pipeline and factors
11
ParkGrid
Dataset
Feature engineering
Time-ordered split
80% / 20%
Random Forest
regressor + classifier
joblib models
/predictions/peak
Factors used (features)
hour
time of day
day_of_week
weekday pattern
is_weekend
weekend flag
capacity_ratio
lot size
rolling_avg_occupancy
mean of last 3 readings
Feature importance
rolling avg
78.7%
hour
17.1%
capacity ratio
3.0%
day of week
0.9%
is weekend
0.3%
Notes: Chronological split so the test set is genuinely future data. The rolling average dominates: recent occupancy is the strongest predictor of near-term occupancy.

## Slide 12
Machine learning results
Held-out later period (5-19 Dec 2016), 7,142 readings
12
ParkGrid
Error, lower is better (occupancy %)
13.41
9.31
Linear Regression
6.23
3.71
Random Forest
RMSE
MAE
0.948
R², Random Forest
baseline linear model: 0.759
0.987
ROC-AUC, peak classifier
accuracy 0.94, F1 0.84
0.95
recall on peak class
misses few real peaks
Notes: Random Forest halves the error of the linear baseline. Limitation: the model learned from large lots; retrain.py adapts it to our 20-slot lot using our own logs. The LSTM in the notebook was not run.

## Slide 13
Technology stack
13
ParkGrid
Backend
FastAPI + Uvicorn
SQLAlchemy 2 + Alembic
PostgreSQL 16
JWT + bcrypt
paho-mqtt, WebSockets
scikit-learn, pandas, joblib
Frontend
React 18 + Vite
Tailwind CSS (dark theme)
Recharts
Three.js + react-three-fiber
qrcode.react, html5-qrcode
React Router, Axios
Infrastructure
Docker + Docker Compose
Mosquitto MQTT broker
7 services, one command
Proposed: AWS IoT Core,
ECS Fargate, RDS, S3,
CloudFront, ElastiCache
Notes: Everything runs from one docker compose command. The cloud items are the proposed deployment, not deployed.

## Slide 14
User dashboard
Live slot map, ML alert and booking
14
ParkGrid
Live slot map over WebSocket
Green free, yellow booked, red occupied
24 h forecast and peak alert
Click a free slot to book it
Notes: Real screenshot of the dashboard with a mix of free, booked and occupied slots.

## Slide 15
Monitor dashboard
3D control room and live activity log
15
ParkGrid
3D view: LED per slot, parked cars, animated gate
Logs: bookings, gate actions, hardware acknowledgements
Present a booking QR to the webcam: the boom lifts and a car drives to its slot
Every event reads as a sentence, not raw telemetry
Notes: Show the 3D scene and the log side by side; both are driven by the same live state.

## Slide 16
Admin control and guest kiosk
Demo resets and walk-in booking
16
ParkGrid
Admin: free one slot or all, with occupant details
Guest kiosk: booking ticket with signed QR
Admin is protected by a shared token; freeing a slot also closes its booking and logs the action
A phone can open the kiosk over the same Wi-Fi, generate a QR, and the laptop webcam scans it
Notes: The kiosk works from a phone on the same network by opening the laptop's IP address.

## Slide 17
Cloud implementation (proposed)
Designed for AWS; not deployed
17
ParkGrid
ESP32 / Pi devices
X.509 certificate each
AWS IoT Core
MQTT over TLS
Backend on ECS Fargate
behind load balancer
Amazon RDS
PostgreSQL
Scheduled
retraining job
S3
model artifacts
ElastiCache Redis
WebSocket pub/sub
CloudFront + S3
React static site
Users: browsers and phones
HTTPS + WSS
CloudWatch
logs + alarms
Why move: managed MQTT and per-device certificates, scaling, backups, HTTPS (browsers need it for camera access off localhost)
Notes: Direct mapping: Mosquitto to IoT Core, Postgres to RDS, backend container to Fargate, in-process WebSocket fan-out to Redis. Secrets move to Secrets Manager.

## Slide 18
Results
Measured on the development laptop (local Docker, median of 8 runs)
18
ParkGrid
13 ms
guest booking request
23 ms
gate scan (entry)
~21 ms
live update reaches browser
0.948
forecast R² (held-out)
Pre-book, scan, enter, scan again, exit: slot green, yellow, red, green
Guest walk-in gets the nearest free slot and a QR
Forged, expired or reused QR is rejected with a reason
Phone generates the QR; laptop webcam scans it on the same Wi-Fi
2D map, 3D LEDs and activity log always agree (one shared state)
Notes: Latency numbers are local loopback figures, so they show the server work is small, not real-network performance.

## Slide 19
Challenges and fixes
Real bugs found while integrating
19
ParkGrid
Symptom
Cause
Fix
Gate scans undone within seconds
Random sensor simulation overwrote real bookings
Gate-controlled slots are held
Slot stayed green after scanning
Camera re-read the QR; 2nd scan meant exit
12 s same-code cooldown
Phone could not open the app
API address hard-coded to localhost
Derive backend host from page host
Database enum errors
SQLAlchemy created enum twice / used names
Explicit enum handling in migration
Notes: The first two are the most instructive: both are interactions between independent parts (simulator vs booking, camera vs scan logic).

## Slide 20
Limitations and future work
20
ParkGrid
Limitations
No physical hardware built
Model trained on large lots; retrain on own logs
LSTM comparison not run (no TensorFlow)
Single backend process, shared admin token
Slots held from booking time, no time-window scheduling
Future work
Build one real ESP32 + HC-SR04 + LED node
Retrain on accumulated entry logs
Cloud deployment with IoT Core and RDS
Payments and dynamic pricing
Licence-plate recognition, mobile app alerts
Notes: Be upfront about what is simulated and what is real.

## Slide 21
Thank you
Questions?
Notes: Open for questions.